## Slide 1: Experiment 2: I/O Interfacing & the 7-Segment Display

## Slide 2: PIC16f84A / PIC16F877

## Slide 3: I/O ports of Microcontroller
PIC microcontrollers’ ports are general-purpose bi-directional digital ports.
The state of TRISx Register controls the direction of the PORTx bits.
A logic one in a bit position configures the PIC to act as an input and if it has a zero to act as an output.
However, a pin can only act as either input or output at any one time but not simultaneously. This means that each pin has a distinct direction state.

## Slide 4: I/O ports of Microcontroller
Input ports “Get Data” from the outside world into the microcontroller while output ports “Send Data” to the outside world.
• LEDs, 7-Segment displays, motors, and LCDs (write mode) that are interfaced to microcontroller’s ports should be configured as output.
• Switches, push buttons, sensors, keypad and LCDs (read mode) that are interfaced to microcontroller’s ports should be configured as input.

## Slide 5: Light Emitting Diodes LED
Light emitting diodes or LEDs are semiconductor light sources used as indicator lamps in many electronic devices.
In order to switch a LED on, forward current must pass from the anode to the cathode, but how to determine which pin of the LED is anode and which is cathode, generally, there are two ways:
1. The longer lead is anode, the shorter is cathode.
2. The cathode has a flat surface
Resistors with values in between 220Ω to 1kΩ are placed in between the voltage source (often 5 to 9V or even more) and the anode to limit the current entering the LED or else it will burn. In this case these resistors are called current limiting resistors

## Slide 6: Seven-Segment Display
If the anode ends of all LEDs are connected together, it is called common anode display.
If the cathodes of all LEDs are connected together, it is called a common cathode display.
To switch a LED on in a common cathode configuration, you have to send logic high to the segment pin.
To switch a LED on in a common anode configuration, you have to send logic low to the segment pin.
since the display is basically LEDs, current limiting resistors are used for each segment.

## Slide 9
The PROTEUS Environment

## Slide 10: Write assembly a code to display the 6 number in the LED and the 7-segment display

## Slide 11
#INCLUDE "P16F84A.INC"
CBLOCK 0X30
V1
V2
ENDC
ORG 0X000
BANKSEL TRISA
MOVLW 0X000
MOVWF TRISA
MOVWF TRISB
BANKSEL PORTA
DISPLAY
          MOVLW 6
MOVWF PORTA
CALL DELAY
MOVLW B'01111101'
MOVWF PORTB
CALL DELAY
GOTO DISPLAY
DELAY
MOVLW 0XFF
MOVWF V1
MOVWF V2
LOOP2
DECFSZ V1, F
GOTO LOOP2
DECFSZ V2, F
GOTO LOOP2
RETURN
END