## Slide 1: CPE 110408362 Embedded Systems Design Lab 3

## Slide 2: Clear/swap
clrw ; W register is cleared. Zero bit (Z) is set.
clrf f ; The contents of register ’f’ are cleared and the Z bit is set.
swapf f, d ;The upper and lower nibbles of register 'f' are exchanged. If 'd' is 0, the result is placed in W register. If 'd' is 1, the result is placed in register 'f‘.
Examples:
clrf TEMP1 ;Clear variable TEMP1
swapf TEMP1, F ;Swap 4-bit nibbles of TEMP1

## Slide 3: Increment/Decrement/Complement
incf f, F(W) ; increment f, putting result in F or W
decf f, F(W) ;decrement f, putting result in F or W
comf f, F(W) ;complement f, putting result in F or W
Examples:
incf TEMP1, F ;Increment TEMP1
incf TEMP1, W ;W <- TEMP1+1; TEMP1 unchanged
decf TEMP1, F ;Decrement TEMP1
comf TEMP1, F ;Change 0s and 1s to 1s and 0s

## Slide 4: Rotate
rlf f, F(W) ; copy f into F or W; rotate F or W left through the carry bit
rrf f, F(W) ; copy f into F or W; rotate F or W right through the carry bit
Examples:
rlf TEMP1, F ; C <- TEMP1.bit(7), TEMP1.bit(i+1) <- TEMP1.bit(i), TEMP1.bit(0) <- C
rrf TEMP1, W ; Copy TEMP1 to W and rotate W right through C, TEMP1 unchanged

## Slide 5: Conditional Branch
The PIC 16series instruction set has four instructions which implement a sort of conditional statement: btfsc , btfss, decfsz and incfsz instructions.
Check for the condition that
1. btfsc f,b : a bit is clear: 0 (Bit Test File, Skip if Clear)
2. btfss f,b : a bit is set one: 1 (Bit Test File, Skip if Set)
3. decfsz f,d: zero flag after decrement the register
4. incfsz f,d: zero flag after increment the register.

## Slide 6: Conditional Branch
movlw 0x09
btfsc VARX, 4
movwf Num1
movwf Num2
You have seen above that if the condition fails, the code will continue normally and both instructions will be executed.
We can check the flags if set or not:
btfss / btfsc STATUS,C
btfss / btfsc STATUS,Z

## Slide 7: Conditional Branch
decfsz f, F(W) ;decrement f, putting result in F or W, skip if zero
incfsz f, F(W) ;increment f, putting result in F or W, skip if zero
(check Zero flag)
Examples:
decfsz TEMP1, F ; Decrement TEMP1, skip if TEMP1==0
incfsz TEMP1, W ; W <- TEMP1+1 , skip if W==0 (TEMP1==0XFF)
This

## Slide 8: Instruction machine code

## Slide 9: Instruction machine code

## Slide 10: Goto/Call
goto label ; Go to labeled instruction(unconditional branch)
call label ; Call labeled subroutine/first, return address (PC+1) is pushed onto the stack.
Examples:
goto There ; Next instruction to be executed is labeled “There”
call Task1 ; Push return address; Next instruction to be executed is labeled “Task1”

## Slide 11: Return/Return from Interrupt
Return ; Return from subroutine
retlw k ; Return from subroutine, putting literal value in W
retfie ; Return from interrupt service routine; re-enable intrrupts
Examples:
return ; Pop return address off of stack
retlw 5 ; Pop return address; W <- 5
retfie ; Pop return address; re-enable interrupts

## Slide 12: Subroutines
  Subroutines are the closest equivalent to functions.
  Subroutines start with a Label giving them a name and end with the instruction return.
  Subroutines can be written anywhere in the program after the org and before the end directives.
  Subroutines are used in the following way: Call subroutineName.
  Subroutines are stored once in the program memory, each time they are used, they are executed from that location.
  Subroutines alter the flow of the program, thus they affect the stack.
  Example :
  domath
  instruction1
  instrucition 2
  return

## Slide 13: Macros
  Macros should be declared before writing the code instructions. It is not recommended to declare macros in the middle of your program.
  Macros are used by only writing their name: macroName
  Each time a macro is called , the call will be replaced by its body, therefore, the program will execute sequentially, the flow of the program will not change. The Stack is not affected.
  macroName macro
    Instruction 1
    Instruction 2
    .
    .
    Instruction n
  endm

## Slide 14
A look-up table is a block of data that is held in the program memory and which can be accessed by the program and used within it. The table is formed as a subroutine.
  Look up tables are a special type of subroutines which are used to retrieve values depending on the input they receive.
  They are invoked in the same as any subroutine: Call tableName
  The retlw instruction is a return instruction with the benefit that it returns a value in W when it is executed.
Look up tables

## Slide 15: Look up tables
lookUpTableName
  addwf PCL, F ;add the number found in the program counter to PCL
  nop
  retlw Value ;if W has 1, execute this
  retlw Value ;if W has 2, execute this
  retlw Value
  …
  retlw Value

## Slide 17
End