## Slide 1: Experiment 4: I/O Interfacing (LEDs)

## Slide 2: PIC16f84A
PORTA - TRISA
PORTB - TRISB

## Slide 3: Configure I/O pins
Whenever you wish to use an I/O pin, you must first configure it to be an output or input pin. Here the function of TRISx register comes in, as the value we write to that register specifies the direction of the corresponding pins (input/output). The x here stands for any port [A, B].
The state of TRISA /TRISB Register controls the direction of the PORTA & PORTB bits.
Writing 1 (High) to a single bit of the TRISx register configures the pin corresponding to this bit to be an input pin.
Writing 0 (Low) to a single bit of the TRISx register configures the pin corresponding to this bit to be an output pin.
Which means that writing the following values to these bits will cause the following effects
Value Bit Effect
1 TRISB1 RB0 pin becomes an input pin
0 TRISB4 RB1 pin becomes an output pin
 TRISB=0X02 (assume the other unconnected pin=0)

## Slide 4: I/O ports of Microcontroller
• LEDs, 7-Segment displays, motors, and LCDs (write mode) that are interfaced to microcontroller’s ports should be configured as output.
• Switches, push buttons, sensors, keypad and LCDs (read mode) that are interfaced to microcontroller’s ports should be configured as input.
MOVLW 0X0F
MOVWF TRISA ; the high nibble of PORTA is input (RA0-RA3), the other bits(RA4,RA5) is output.
MOVLW B’11001010’
MOVWF TRISB ; bits 0,2,4,5 as output… bits 1,3,6,7 as input.

## Slide 5: Light Emitting Diodes LED
Light emitting diodes or LEDs are semiconductor light sources used as indicator lamps in many electronic devices.
In order to switch a LED on, forward current must pass from the anode to the cathode, but how to determine which pin of the LED is anode and which is cathode, generally, there are two ways:
1. The longer lead is anode, the shorter is cathode.
2. The cathode has a flat surface
Resistors with values in between 220Ω to 1kΩ are placed in between the voltage source (often 5 to 9V or even more) and the anode to limit the current entering the LED or else it will burn. In this case these resistors are called current limiting resistors

## Slide 6
The PROTEUS Environment

## Slide 7: Write assembly a code to display the 2 and 9 numbers in the LED continuously

## Slide 8: Our code
#INCLUDE "P16F84A.INC"
CBLOCK 0X30
V1
V2
ENDC
ORG 0X000
BANKSEL TRISA
MOVLW 0X000
MOVWF TRISA
BANKSEL PORTA
DISPLAY
          MOVLW 2
MOVWF PORTA
CALL DELAY
          MOVLW 9
MOVWF PORTA
CALL DELAY
GOTO DISPLAY
DELAY
MOVLW 0XFF
MOVWF V1
MOVWF V2
LOOP2
DECFSZ V1,1
GOTO LOOP2
DECFSZ V2,1
GOTO LOOP2
RETURN
END