## Slide 2: CPE 110408362 Embedded Systems Design Lab 1: Introduction to PIC Microcontroller

## Slide 3: What is Microcontroller
A Microcontroller is a compact Microcomputer or “Computer on chip”.
It’s a single IC that contains :
      Processor core.
      ROM.
      RAM.
      I/O control unit.
Microcontrollers are Designed for Embedded applications (mainly).
The main difference between a Microprocessor and a Microcontroller is that a Microcontroller has an internal bus with built in memory and peripherals.
Notes: Microprocessor is an IC which has only the CPU inside them i.e. only the processing powers such as Intel’s Pentium 1,2,3,4, core 2 duo, i3, i5 etc. These microprocessors don’t have RAM, ROM, and other peripheral on the chip. A system designer has to add them externally to make them functional.

## Slide 4: comparison between Computer and MCU

## Slide 5: Microcontrollers Architecture
Von Neumann Architecture:
    The system has single memory for data and program to be executed.
    Two clock cycles needed to complete an instruction.
    Pipelining is not possible with this architecture.
Harvard Architecture :
    Two separate memories for storing data and program.
    Instruction needs one cycle if appropriate pipelining strategies are implemented.

## Slide 6: Microcontrollers Architecture

## Slide 7: What is the PIC Microcontroller
  The Programmable Interface Controller (PIC) is a microcontroller developed by “Microchip Technology”.
  Harvard Architecture.
  PICs are available with various on-board peripherals (serial communication modules, UARTs, motor control kernels, etc.).
  PIC microcontroller is can be re-programed as they use flash memory.
  PIC microcontroller can be programed using assembly language or a high-level language such as C as it is much easier to use.

## Slide 8: PIC16F84A Features
    Only 35 single word instructions
    Operating speed: DC - 20 MHz clock input
    1024 words of program memory
    14-bit wide instruction words
    8-bit wide data bytes
    15 Special Function Hardware registers
    Eight-level deep hardware stack
    13 I/O pins with individual direction control
    High current sink/source for direct LED drive
    10,000 erase/write cycles Enhanced FLASH
    Program memory typical
    Low power, high speed technology
Notes: Max cpu speed =20MHZ

## Slide 9: Figure 2: PIC 16F84A Block diagram

## Slide 10: CPU
A PIC CPU consists of several units such as ALU, Instruction Decoder, Control Unit, etc.
Support Reduce Instruction Set Computer (RISC) Architecture.
Execution Time is same for most of instructions.
Notes: RISC :devices with only basic function instructions

## Slide 11: Memory Map
A memory map shows all available registers (in data memory) of a certain PIC along with their addresses.
The registers are organized as a table format and has two parts:
  Upper part: which lists all the Special Function Registers (SFR) in a PIC; these registers normally have specific functions and are used to control the PIC operation
  2. Lower part: which shows the General Purpose Registers (GPR) in a PIC; GPRs are data memory locations that the user is free to use as he wishes.

## Slide 13: Bank Switching
The memory map is divided into two columns, each column is called a bank.
The two banks are called : bank 0 and bank 1.
In order to access bank 1, we have to switch to that bank first and same for bank 0.
Bank Switching can be Performed using special instruction will be discussed later.

## Slide 14: What are the banks for?
14-bit instructions use 7 bits to address a location
Memory space is organized in 128Byte banks.
Bank 1 is used to control the actual operation of the PIC
Bank 0 is used to manipulate the data.

## Slide 15: Some Special Function Registers
  W, the working register
  To move values from one register to another register, the value must pass through the W register.
FSR, File Select Register
  Indirect data memory addressing pointer.
PC, the Program Counter
  PCL and PCLATH

## Slide 16: PIC Assembly Instruction Set(I)

## Slide 17: Instructions Overview
Instruction set contains 35 instructions.
Each is single word long (14 bits).
Byte-oriented OPCODE f, F(W)
  Source f: name of a SFR or a RAM variable
  Destination F(W):
    F if the destination is to be the same as the source register
    W if the destination is to be the working register
Bit-oriented OPCODE f, b
  Bit address b (0≤b≤7)
Literal and control OPCODE k
  Literal value k

## Slide 19: Movement instructions
Moving constants to the working register (Loading)
Moving values from the data memory to the working register (Loading)
Moving values from the working register to the data memory (Storing)

## Slide 20: MOVLW: moves a literal (constant) to the working register
1. MOVLW 05 ; moves the constant 5 to the working register
2. MOVLW 10 ; moves the constant 16 to the working register.
3. MOVLW d’10’ ; moves the decimal value 10 to the working register.
4. MOVLW .10 ; moves the decimal value 10 to the working register.
5. MOVLW b ’10011110’ ; moves the binary value 10011110 to the W.
6. MOVLW O ’76’ ; moves the octal value 76 to the working register.
7. MOVLW A’g’ ; moves the ASCII value g to the working register.
8. MOVLW 0xAB ; moves the constant ABh to the working register
9. MOVLW H’7F’ ; moves the constant 7Fh to the working register
10.MOVLW CD ; WRONG, if a hexa number starts with a character, you should write it as 0CD or 0xCD or H’CD’

## Slide 22: MOVWF: COPIES the value found in the working register into the data memory, instructions
1. MOVWF 01 ; COPIES the value found in W to TMR0
2. MOVWF 05 ; COPIES the value found in W to PORTA
3. MOVWF 0C ; COPIES the value found in W to a GPR (location 0C)
4. MOVWF 32 ; COPIES the value found in W to a GPR (location 32)
5. MOVWF 52 ; WRONG, out of data memory range of the PIC 16F84a (GPR range is from 0C-4F and 8C to CF)

## Slide 23: MOVF: COPIES a value found in the data memory to the working register OR to itself.
1. MOVF 05, 0 ; copies the content of PORTA to the working register.
2. MOVF 2D, 0 ; copies the content of the GPR 2D the working register
3. MOVF 05, 1 ; copies the content of PORTA to itself
4. MOVF 2D, 1 ; copies the content of the GPR 2D to itself

## Slide 24
                MPLAB