## Slide 1: CPE 110408362 Embedded Systems Design Lab 2

## Slide 2: Directives
Directives are not instructions. They are assembler commands that appear in the source code but are not usually translated directly into opcodes.
They are used to control the assembler: its input, output, and data allocation.
They are not converted to machine code (.hex file) and therefore not downloaded to the PIC.

## Slide 3: END
The “END” command is a directive which tells the MPLAB IDE that we have finished our program. It has nothing to do with neither the actual program nor the PIC.
The END should always be the last statement in your program Anything which is written after the end command will not be executed and any variable names will be undefined.

## Slide 4: Equate directive “EQU”
The equate directive is used to assign labels to numeric values. They are used to DEFINE CONSTANTS or to ASSIGN NAMES TO MEMORY ADDRESSES OR INDIVIDUAL BITS IN A REGISTER and then use the name instead of the numeric address.
Timer0 equ 01
Intcon equ 0B
Workrg equ 0
Temp equ 20

## Slide 5: Example
Movlw 5 ; move the constant 5 to the working register
Movwf Timer0 ; copy the value 5 from working register to TMR0 (address 01)
Movlw 2 ; move the constant 2 to the working register
Movwf Intcon ; copy the value 2 from working register to INTCON (address 0B)
Movf Timer0, Workrg ; copy back the value 5 from TMR0 to working register
Nop ; this instruction does nothing End

## Slide 6
#include “P16F84A.inc”
The only condition when using the include directive is to use the names as Microchip defined them which are ALL CAPITAL LETTERS and AS WRITTEN IN THE DATA SHEET. If you don't do so, the MPLAB will tell you that the variable is undefined!
#include “P16F84A.inc”
Movlw 5 ; move the constant 5 to the working register
Movwf TMR0 ; copy the value 5 from working register to TMR0 address 01
Include

## Slide 7: Cblock
The “cblock” is used to define variables in the data memory.
The cblock defines variables in sequential locations, see the following declaration
  Cblock 0x35
  VarX
  VarY
  VarZ
  endc
Here, VarX has the starting address of the cblock, which is 0x35, VarY has the sequential address 0x36 and VarZ the address of 0x37 What if I want to define variable at locations which are not sequential, that is some addresses are at 0x25 others at 0x40? Simply use another cblock statement, you can add as many cblock statements as you need.

## Slide 8: org
The origin directive is used to place the instruction which exactly comes after it at the location it specifies.
Examples:
Org 0x00
Movlw 05 ;This instruction has address 0 in program memory
Addwf TMR0 ;This instruction has address 1 in program memory
Org 0x04 ;Program memory locations 2 and 3 are empty, skip to address 4 where it contains
Addlw 08 ;this instruction Org 0x13 ;WRONG, org only takes even addresses
In This Course, Never Use Any Origin Directives Except For Org 0x00 And 0x04, Changing Instructions’ Locations In The Program Memory Can Lead To Numerous Errors.

## Slide 9: Bank Switching
#include “P16F84A.inc”
Movlw 5 ; move the constant 5 to the working register
Movwf TRISA ;copy the value 5 from working register to TRISA address 85)
After simulation, you will notice that TRISA was not filled with the values 5! But why?
Banksel TRISA
Movlw 5 ; move the constant 5 to the working register
Movwf TRISA ; copy the value 5 from working register to TRISA (address 85)

## Slide 11: Bank Switching
We have to switch to that bank1 first.
We can change RP0 by using the bcf/bsf instructions
BCF STATUS, RP0 ;RP0 in STATUS is 0 ->switch to bank 0
BSF STATUS, RP0 ;RP0 in STATUS is 1 ->switch to bank 1

## Slide 12: Single Bit Manipulation
bcf f,b
  Operation: Clear bit b of register f, where b=0 to 7.
bsf f,b
  Operation: Set bit b of register f, where b=0 to 7.
  Examples:
  bcf PORTB, 0 ; Clear bit 0 off PORTB
  bsf STATUS, C ; Set the Carry bit
  bcf STATUS, RP1 ;
  bsf STATUS, RP0 ; Select Bank 1

## Slide 13: FLAGS
The PIC 16 series has three indicator flags found in the STATUS register; they are the C, DC, and Z flags.
Not all instructions affect the flags; some instructions affect some of the flags while others affect all the flags.
The MOVLW and MOVWF do not affect any of the flags while the MOVF instruction affects the zero flag. Copying the register to itself does make sense now because if the file has the value of zero the zero flag will be one.
Therefore the MOVF instruction is used to affect the zero flag and consequently know if a register has the value of 0. (Suppose you are having a down counter and want to check if the result is zero or not).

## Slide 15: Logical and Arithmetic Instructions
There are the ADD, SUB, AND, XOR, IOR (the ordinary Inclusive OR).
cblock 0x20
TEMP1
endc
addlw 5 ; W <= 5+W
addwf TEMP1, F ; TEMP1 <- TEMP1+W

## Slide 17: Addition/Subtraction
sublw 5 ; W <= 5-W (not W <= W-5 )
subwf TEMP1, F ; TEMP1 <= TEMP1 - W

## Slide 18: Logical operations
Examples:
andlw B’00000111’ ; force upper 5 bits of W to zero
andwf TEMP1, F ; TEMP1 <- TEMP1 AND W
andwf TEMP1, W ; W <- TEMP1 AND W
iorlw B’00000111’ ; force lower 3 bits of W to one
iorwf TEMP1, F ; TEMP1 <- TEMP1 OR W
xorlw B’00000111’ ; complement lower 3 bits of W
xorwf TEMP1, W ; W <- TEMP1 XOR W

## Slide 19: Example Program:
Implementing the function Result = (X + Y) xor Z