## Slide 1: Sequential Circuits in Verilog

## Slide 2: D Flip-Flop
module D_ff(input clk, input d, output reg q);
always @ (negedge clk)
q <= d; // pronounced “q gets d”
endmodule

## Slide 3: D Flip-Flop with Asynchronous Reset
module D_ff (input clk, input reset, input d, output reg q);
always @ (negedge clk, posedge reset)
begin
if (reset == 1) q <= 0; // when reset
else q <= d; // when clk
end
endmodule

## Slide 4: D Flip-Flop with Synchronous Reset
module D_ff (input clk, input reset, input d, output reg q);
always @ (posedge clk)
begin
if (reset == 1) q <= 0; // when reset
else q <= d; // when clk
end
endmodule

## Slide 5: D Flip-Flop with Enable and Reset
module D_ff (input clk, input reset, input d, input en, output reg q);
always @ (negedge clk, posedge reset)
begin
if (reset == 1) q <= 0; // when reset
else if (en) q <= d; // when enble and clk
end
endmodule

## Slide 6: T Flip-Flop
module T_ff (input clk, input reset, output q);
wire d;
D_ff dff1 (clk, reset, d, q);
not n1(d,q);
endmodule

## Slide 7: Structural Model : 4-bit Counter
module ripple_carry_counter (q, clk, reset);
output [3:0] q;
input clk, reset;
T_ff tff0(q[0], clk, reset);
T_ff tff1(q[1], q[0], reset);
T_ff tff2(q[2], q[1], reset);
T_ff tff3(q[3], q[2], reset);
endmodule

## Slide 8: Finite State Machine
Each FSM consists of three separate parts:
  next state logic
  state register
  output logic

## Slide 9: FSM Verilog Implementation
module FSM (q, i, clk, rst);
  input clk,i, rst;
  output q;
  reg q;
  reg [1:0] state, nextstate;
  //The parameter descriptions are optional, it makes reading easier
  parameter S0 = 2'b00, S1 = 2'b01,S2 = 2'b10;

## Slide 10: FSM Verilog Implementation: Single Always Block

## Slide 11: FSM Verilog Implementation: 3-Always Block
endmodule
if (state == s2) q = 1;
else q =0;
This is the recommended implementation of FSM.
Last always (output) can be coded with assign statement