## Slide 1: Half-Wave Dipole
Previously we developed expressions for the electric and magnetic fields radiated by a Hertzian dipole of length .
We now use these expressions as building blocks to obtain expressions for the fields radiated by a half-wave dipole antenna, so named because its length .

## Slide 2: The half-wave dipole consists of a thin wire fed at its center by a generator connected to the antenna terminals via a transmission line. The current flowing through the wire has a symmetrical distribution with respect to the center of the dipole, and the current is zero at its ends. Mathematically, i(t) is given by
Each length element dz of half-wave dipole is like a Hertzian dipole, radiating a field (derived previously):

## Slide 3
For the entire dipole, the total radiated field is:
Before we calculate this integral, we make the following two approximations:
1-The first relates to the magnitude part of the spherical propagation factor, 1/s. In Fig. 9-14(b), the distance s between the current element and the observation point Q is considered so large in comparison with the length of the dipole that the difference between s and R may be neglected in terms of its effect on 1/s. Hence, we may set 1/s ≈ 1/R, and by the same argument we set θs ≈ θ. The error between s and R is a maximum when the observation point is along the z axis and it is equal to λ/4 (corresponding to half of the antenna length). If R >> λ, this error will have an insignificant effect on 1/s.
2- The second approximation is associated with the phase factor . An error in distance ∆ corresponds to an error in phase k = (2π/λ)(λ/4) = π/2. As a rule of thumb, a phase error greater than π/8 is considered unacceptable because it may lead to a significant error in the computed value of the field . Hence, the approximation s ≈ R is too crude for the phase factor and cannot be used. A more tolerable option is to use the parallel-ray approximation given by:

## Slide 4: Half-Wave Dipole (cont.)
Integration leads to:
The radiation pattern of the half-wave dipole exhibits roughly the same doughnut-like shape shown earlier in Fig. 9-7 for the short dipole.

## Slide 5: Radiation Pattern of Half-Wave Dipole
Radiation pattern resembles that of the Hertzian dipole. Its beamwidth is slightly narrower, 78 degrees compared with 90 degrees for the Hertzian dipole.

## Slide 6: Other Half-Wave Dipole Properties
1. Directivity
Numerical integration gives:
2. Radiation Resistance
This is very important, because it makes it easy to match the antenna to a 75-Ω transmission line. In contrast, the radiation resistance of a dipole whose length is much shorter than a wavelength is on the order of 0.1 Ω or less.

## Slide 10: Quarter-Wave Monopole
When placed over a conducting ground plane, a quarter-wave monopole antenna excited by a source at its base [Fig.9-15(a)] exhibits the same radiation pattern in the region above the ground plane as a half-wave dipole in free
space.
the radiation is limited to the upper half space defined by 0 ≤ ≤ π/2. Hence, a monopole radiates only half as much power as the dipole.
However, its radiation resistance if only half of that of a half-wave dipole, namely 36.5 Ω.

## Slide 11
The simplest mobile antenna is a quarter wave whip antenna. It consists of a single vertical element, approximately 1/4 wavelength long, mounted onto the metal roof of an automobile, and is called a monopole. The roof acts as a “ground plane” reflector so that the antenna radiation pattern emulates a dipole antenna. At VHF low band (50 MHz), a quarter wave monopole antennas are about 5 feet long. As the frequency is increased, the length of a monopole antenna is reduced. At 850 MHz, a monopole is only 3.5 inches long.

## Slide 14: Dipole of Arbitrary Length
We need to consider the more general case of a linear dipole of arbitrary length l, relative to λ. For a center-fed dipole, as depicted in Fig. 9-16, the currents flowing through its two halves are symmetrical and must go to zero at its ends.

## Slide 22: Antenna Effective Area
The effective antenna area is a theoretical value which is a measure of how effective an antenna is at receiving power. The effective aperture/area can be calculated by knowing the gain of the receiving antenna. (Other commonly used names for Ae include effective aperture and receiving cross section).
How a receiving antenna extracts energy from an incident wave and delivers it to a load.

## Slide 23: Antenna Effective Area

## Slide 27: Friis Transmission Formula

## Slide 28
Initially, we consider the case where the two antennas are oriented such that the peak of the radiation pattern of each antenna points in the direction of the other.

## Slide 32
Example 9-4 (cont.)

## Slide 33: Exercise: A transmitter produces 50W of power. If this power is applied to a unity gain antenna with 900 MHz carrier frequency, a) find the received power at a (line of sight) LOS distance of 100 m from the antenna. B) What is the received power at 10 km. Assume unity gain for the receiver antenna.
Answer:
Pr = 3.5 x 10-6 W
Pr (10 km) = Pr (100 m) x (100/10000)2
= 3.5 x 10-6 x (1/100)2
= 3.5 x 10-10 W