## Slide 1: Antenna Radiation Characteristics
1. By virtue of reciprocity, a receiving antenna has the same directional antenna pattern as the pattern that it exhibits when operated in the transmission mode.
2. Total Radiated Power
Differential area
Solid Angle
Power radiated through dA
Total Radiated Power

## Slide 2
where F(θ,φ) is the normalized radiation intensity.
The 4π symbol under the integral sign is used as an abbreviation for the indicated limits on θ and φ.
Formally, Prad is called the total radiated power.

## Slide 3: Antenna Pattern Representative Plots
Each specific combination of the zenith angle θ and the azimuth angle φ denotes a specific direction in the spherical coordinate system of Fig. 9-8.
The normalized radiation intensity F(θ,φ) characterizes the directional pattern of the energy radiated by an antenna, and a plot of F(θ,φ) as a function of both θ and φ constitutes a three-dimensional pattern, an example of which is
shown in Fig. 9-9.
Often, it is of interest to characterize the variation of F(θ,φ) in the form of two-dimensional plots in specific planes in the spherical coordinate system.
The two planes most commonly specified for this purpose are the elevation and azimuth planes.

## Slide 4: Example of 3-D Pattern
F (dB) = 10 log F
Principal planes:
1. Elevation plane (x-z and y-z planes)
2. Azimuth plane (x-y plane)

## Slide 5
The elevation plane, also called the θ plane, is a plane corresponding to a constant value of φ. For example, φ = 0 defines the x–z plane and φ = 90◦ defines the y–z plane, both of which are elevation planes (Fig. 9-8). A plot of F(θ,φ) versus θ in either of these planes constitutes a two-dimensional pattern in the elevation plane. This is not to imply, however, that the elevation-plane pattern is necessarily the same in all elevation planes.
The azimuth plane, also called the φ plane, is specified by θ = 90◦ and corresponds to the x–y plane. The elevation and azimuth planes are often called the two principal planes of the spherical coordinate system.
Some antennas exhibit highly directive patterns with narrow beams, in which case it is often convenient to plot the antenna pattern on a decibel scale by expressing F in decibels:
F (dB) = 10 log F

## Slide 6: Polar and Rectangular Plots

## Slide 7
As an example, the antenna pattern shown in Fig. 9-10(a) is plotted on a decibel scale in polar coordinates, with intensity as the radial variable. This format permits a convenient visual interpretation of the directional distribution of the radiation lobes.
Another format commonly used for inspecting the pattern of a narrow-beam antenna is the rectangular display shown in Fig. 9-10(b), which permits the pattern to be easily expanded by changing the scale of the horizontal axis. These plots represent the variation in only one plane in the observation sphere, the φ = 0 plane. Unless the pattern is symmetrical in φ, additional patterns are required to define the overall variation of F(θ,φ) with θ and φ.
The pattern shown in Fig. 9-10(a) indicates that the antenna is fairly directive, since most of the energy is radiated through a narrow sector called the main lobe which includes the direction of maximum radiation (sometimes called the boresight direction). In addition to the main lobe, the pattern exhibits several side lobes and back lobes of radiation diametrically opposite the main lobe as well.
For most applications, these extra lobes are considered undesirable because they represent wasted energy for transmitting antennas and potential interference directions for receiving antennas.

## Slide 8: Beam Dimensions
1. Pattern solid angle
For an antenna with a single main lobe, the pattern solid angle p describes the equivalent width of the main lobe of the antenna pattern (Fig. 9-11). It is defined as the integral of the normalized radiation intensity F(θ,φ) over a sphere:

## Slide 9
2. Half-power beamwidth
Since 0.5 corresponds to ‒3 dB, the half power beamwidth is also called the 3-dB beamwidth.
To characterize the width of the main lobe in a given plane, the term used beamwidth. The half-power beamwidth, or simply the beamwidth β, is defined as the angular width of the main lobe between the two angles at which the magnitude of F(θ,φ) is equal to half of its peak value (or −3 dB on a decibel scale).

## Slide 10: Antenna Directivity D
Antenna pattern solid angle
Directivity
The directivity D of an antenna is defined as the ratio of
its maximum normalized radiation intensity, Fmax (which by definition is equal to 1), to the average value of F(θ,φ) over all directions (4π space):

## Slide 11
D can be expressed as:
or

## Slide 12: Antennas with Single Main Lobe
Equivalent Solid Angle

## Slide 13
Cont.

## Slide 14
(cont.)

## Slide 16
An antenna with high radiation efficiency therefore has high associated radiation resistance compared with the losses. The antenna is said to be resonant if its input reactance Xa = 0. If the source impedance, Zs = Rs + jXs, and the total antenna impedance, Za =++jXa, are complex conjugates, i.e. then the source is matched to the antenna and a maximum of the source power is delivered to the antenna. If the match is not ideal, then the degree of mismatch can be measured using the reflection coefficient  (or ), defined by:
where Vr and Vi are the amplitudes of the waves reflected from the antenna to the transmitter and incident from the transmitter onto the antenna terminals, respectively.

## Slide 17: Radiation Resistance and Efficiency
The equivalent circuit of a transmitter and its associated antenna is shown in Fig. The resistive part of the antenna impedance is split into two parts, a radiation resistance and a loss resistance .
The power dissipated in the radiation resistance is the power actually radiated by the antenna, and the loss resistance is power lost within the antenna itself. This may be due to losses in either the conducting or the dielectric parts of the antenna.
Although only the radiated power normally serves a useful purpose, it is useful to define the radiation efficiency  of the antenna as


## Slide 18
It is also common to measure the mismatch via the voltage standing wave ratio (VSWR), with an optimum value of 1:
It is common to design antennas to a standard input impedance of either 50  or 75  .
Note: Most coaxial cables and connectors in common use have a 50  characteristic impedance, with an exception being the 75  cable used in television systems. The reasoning behind these choices is that an air-filled coaxial line has minimum attenuation for a characteristic impedance of about 77 , while maximum power capacity occurs for a characteristic impedance of about 30 . A 50  characteristic impedance thus represents a compromise between minimum attenuation and maximum power capacity.

## Slide 19
S-parameters describe the input-output relationship between ports (or terminals) in an electrical system. For instance, if we have 2 ports (intelligently called Port 1 and Port 2), then:
S12 represents the power transferred from Port 2 to Port 1.
S21 represents the power transferred from Port 1 to Port 2.
In general, SNM represents the power transferred from Port M to Port N in a multi-port network.
A port can be loosely defined as any place where we can deliver voltage and current. So, if we have a communication system with two radios (radio 1 and radio 2), then the radio terminals (which deliver power to the two antennas) would be the two ports. S11 then would be the reflected power radio 1 is trying to deliver to antenna 1. S22 would be the reflected power radio 2 is attempting to deliver to antenna 2. And S12 is the power from radio 2 that is delivered through antenna 1 to radio 1. Note that in general S-parameters are a function of frequency (i.e. vary with frequency).

## Slide 20
As an example, consider the above two-port network:
S21 represents the power received at antenna 2 relative to the power input to antenna 1. For instance, S21= 0 dB implies that all the power delivered to antenna 1 ends up at the terminals of antenna 2. If S21= -10 dB, then if 1 Watt (or 0 dB) is delivered to antenna 1, then -10 dB (0.1 Watts) of power is received at antenna 2.
In practice, the most commonly quoted parameter in regards to antennas is S11. S11 represents how much power is reflected from the antenna, and hence is known as the reflection coefficient (sometimes written as gamma: or return loss). If S11 = 0 dB, then all the power is reflected from the antenna and nothing is radiated. If S11 = -10 dB, this implies that if 3 dB of power is delivered to the antenna, -7 dB is the reflected power. The remainder of the power was "accepted by" or delivered to the antenna. This accepted power is either radiated or absorbed as losses within the antenna. Since antennas are typically designed to be low loss, ideally the majority of the power delivered to the antenna is radiated. (also VSWR, which is directly related to S11)

## Slide 21
The return loss would typically be measured using a Vector Network Analyzer (VNA), which can plot S11. The figure implies that the antenna radiates best at 2.5 GHz, where S11 = -10 dB. Further, at 1.5 GHz the antenna will radiate virtually nothing, as S11 is close to 0 dB (so all the power is reflected). The antenna bandwidth can also be determined from the above figure. If the bandwidth is defined as the frequency range where S11 is to be less than -6 dB, then the bandwidth would be roughly 1 GHz, with 3 GHz the high end and 2 GHz the low end of the frequency band.
As an example, consider the plot of S11 in the following figure:

## Slide 23: Example:

## Slide 25: Radiation Efficiency and Gain
Radiation efficiency
Antenna gain G

## Slide 26: Antenna Radiation and Loss Resistances

## Slide 27
Cont.

## Slide 28: Example 9-3 (cont.)
For any antenna:
For the Hertzian dipole:

## Slide 29: Please try these

## Slide 30: ELECTROMAGNETIC SPECTRUM & BandWidth (BW)
The basic resource exploited in wireless communication systems is the electromagnetic spectrum, illustrated in Fig below. Practical radio communication takes place at frequencies from around 3 kHz [kilohertz] to 300 GHz [gigahertz], which corresponds to wavelengths in free space from 100 km to 1 mm.

## Slide 31
Table 1.1 defines two conventional ways of dividing the spectrum into frequency bands. The frequencies chosen for new systems have tended to increase over the years as the demand for wireless communication has increased; this is because enormous bandwidths are available at the higher frequencies. This shift has created challenges in the technology needed to support reliable communications, but it does have the advantage that antenna structures can be smaller in absolute size to support a given level of performance.

## Slide 32: BandWidth (BW)
BW describes the range of frequencies over which the antenna can properly radiate or receive energy. Often, the desired bandwidth is one of the determining parameters used to decide upon an antenna. For instance, many antenna types have very narrow bandwidths and cannot be used for wideband operation.
BW is typically quoted in terms of VSWR. For instance, an antenna may be described as operating at 100-400 MHz with a VSWR<1.5. This statement implies that the reflection coefficient is less than 0.2 across the quoted frequency range. Hence, of the power delivered to the antenna, only 4% of the power is reflected back to the transmitter. Alternatively, the return loss:
S.
(Note: that the above does not imply that 96% of the power delivered to the antenna is transmitted in the form of EM radiation; losses must still be taken into account).

## Slide 33
Also, the radiation pattern will vary with frequency. In general, the shape of the radiation pattern does not change radically.
There are also other criteria which may be used to characterize bandwidth. This may be the polarization over a certain range, for instance, an antenna may be described as having circular polarization with an axial ratio < 3dB (less than 3 dB) from 1.4-1.6 GHz. This polarization bandwidth sets the range over which the antenna's operation is approximately circularly polarized.
The bandwidth is often specified in terms of its Fractional Bandwidth (FBW). The FBW is the ratio of the frequency range (highest frequency minus lowest frequency) divided by the center frequency. The antenna Q also relates to bandwidth (higher Q is lower bandwidth, and vice versa).

## Slide 34
The Q of an antenna is a measure of the bandwidth of an antenna relative to the center frequency of the bandwidth. If the antenna operates over a band between f1 and f2 with center frequency fc=(f1+f2)/2, then the Q is given by:
Antennas with a high Q are narrowband, antennas with a low Q are wideband. The higher the value of Q, the more sensitive the input impedance is to small changes in frequency.

## Slide 35
To give some concrete examples of bandwidth, here is a table of the bandwidths for common antenna types. This will answer such questions as "what is the bandwidth of a dipole antenna" and "which antenna has a higher bandwidth - a patch or a spiral antenna". For a fare comparison, we set the center frequency for each antenna to 1 GHz (1000 MHz).
As can be seen from Table I, the bandwidth for antennas can vary widely. Patch (Microstrip) Antennas are very low bandwidth, while spiral antennas have a very large BW.

## Slide 36: POLARISATION
 The alignment of the electric field vector of a plane wave relative to the direction of propagation defines the polarisation of the wave.
 In Fig the electric field is parallel to the x axis, so this wave is x polarised. This wave could be generated by a straight wire antenna parallel to the x axis. An entirely distinct y-polarised plane wave could be generated with the same direction of propagation and recovered independently of the other wave using pairs of transmit and receive antennas with perpendicular polarisation.
 If the wave is generated by a vertical wire antenna (H field horizontal), then the wave is said to be vertically polarised; a wire antenna parallel to the ground (E field horizontal) primarily generates waves that are horizontally polarised.
 The waves described so far have been linearly polarised, since the electric field vector has a single direction along the whole of the propagation axis.

## Slide 37
 If two plane waves of equal amplitude and orthogonal polarisation are combined with a 90 degree phase difference, the resulting wave will be circularly polarised (CP), in that the motion of the electric field vector will describe a circle centred on the propagation vector.
 The field vector will rotate by 360 degree for every wavelength travelled. Circularly polarised waves are most commonly used in satellite communications, since they can be generated and received using antennas which are oriented in any direction around their axis without loss of power.
 They may be generated as either right-hand circularly polarised (RHCP) or left-hand circularly polarised (LHCP).

## Slide 38
 In the most general case, the component waves could be of unequal amplitudes or at a phase angle other than 90 degree. The result is an elliptically polarised wave, where the electric field vector still rotates at the same rate but varies in amplitude with time, thereby describing an ellipse. In this case, the wave is characterised by the ratio between the maximum and minimum values of the instantaneous electric field, known as the axial ratio, AR,
AR is defined to be positive for left-hand polarisation and negative for right-hand polarisation. These various polarisation states are illustrated in Fig