## Slide 1: 9. Radiation & Antennas
7e Applied EM by Ulaby and Ravaioli

## Slide 2: Overview

## Slide 3
Antennas are made in various shapes and sizes (Fig. 9-2) and are used in radio and television broadcasting and reception, radio-wave communication systems, cellular telephones, radar systems, and anticollision automobile sensors, among many other applications.
The radiation and impedance properties of an antenna are governed by its shape, size, and material properties.
The dimensions of an antenna are usually measured in units of λ of the wave it is launching or receiving; a 1 m long dipole antenna operating at a wavelength λ = 2 m exhibits the same properties as a 1 cm long dipole operating at λ = 2 cm (Hence, in most of our discussions in this chapter, we refer to antenna dimensions in wavelength units).

## Slide 4: Examples of Antennas

## Slide 6
Our project:
PIFA (Planar Inverted F Antenna) is one of the most used in mobile devices, fundamentally for it reduced size. (details later)

## Slide 7: MIMO, or Multiple Input Multiple Output, utilizes multiple antennas at both the transmitter and the receiver (smartphone) to increase link reliability and spectral efficiency.

## Slide 8: Antenna Properties
1. An antenna is a transducer that converts a guided wave propagating on a transmission line into an electromagnetic wave propagating in an unbounded medium (usually free space), or vice versa.
2. Most antennas are reciprocal devices, exhibiting the same radiation pattern for transmission as for reception.
3. Being a reciprocal device, an antenna, when operating in the receiving mode, can extract from an incident wave only that component of the wave whose electric field matches the antenna polarization state.

## Slide 9: RECIPROCITY THEOREM
Statement: "In any linear and bilateral network consisting the linear and bilateral impedance the ratio of voltage V applied between any two terminals to the current I measured in any branch is same as the ratio V to I obtained by interchanging the positions of voltage source and the ammeter used for current measurement."
The ratio V to I is generally called transfer impedance. Here both the voltage source and ammeter are assumed to have zero impedance. This theorem holds good if both, voltage source and ammeter have same internal impedances.
This theorem is equally useful in the circuit theory as well as the field theory. Let us consider that the antenna system is represented as a 4-terminal network with pair of terminals at input and another pair of terminals at the output. It is also called two port network as pair of terminals is defined as port. The 4-terminal representation of the antenna system is as shown in the Fig. 10(a). Note that the pair of terminals or ports are nothing but the terminals of the dipoles as shown in the Fig. 10 (b).

## Slide 10
The directional function characterizing the relative distribution of power radiated by an antenna is known as the antenna radiation pattern, or simply the antenna pattern.
An isotropic antenna is a hypothetical antenna that radiates equally in all directions, and it is often used as a reference radiator when describing the radiation properties of real antennas.

## Slide 12: Far-Field Approximation
1. In close proximity to a radiating source, the wave is spherical in shape, but at a far distance, it becomes approximately a plane wave as seen by a receiving antenna.
2. The far-field approximation simplifies the math.
3. The distance beyond which the far-field approximation is valid is called the far-field range (will be defined later).

## Slide 13: Near and Far Field Regions
The field patterns, associated with an antenna, change with distance and are associated with two types of energy: radiating energy and reactive energy. Hence, the space surrounding an antenna can be divided into three regions.
antenna

## Slide 15: Radiation sources
Radiation sources fall into two categories: currents and aperture fields.
The dipole and loop antennas [Fig. 9-2(a) and (c)] are examples of current sources; the time-varying currents flowing in the conducting wires give rise to the radiated electromagnetic fields.
A horn antenna [Fig. 9-2(g)] is an example of the second group because the electric and magnetic fields across the horn’s aperture serve as the sources of the radiated fields. The aperture fields are themselves induced by time-varying currents on the surfaces of the horn’s walls, and therefore ultimately all radiation is due to time-varying currents.
The choice of currents or apertures as the sources is merely a computational convenience arising from the structure of the antenna. We will examine the radiation processes associated with both types of sources.