## Slide 1: Radiation by Aperture Antennas

## Slide 2
Instead of calculating the radiated fields E and H at Q due to currents in the antenna, with apertures it is also possible to relate the radiated fields to the electric field distribution across the aperture. (The source of radiation is the electric-field distribution across the aperture)
The horn antenna shown above is connected to a source through a coaxial transmission line, with the outer conductor of the line connected to the metal body of the horn and the inner conductor made to protrude, through a small hole, partially into the throat end of the horn. The protruding conductor acts as a monopole antenna, generating waves that radiate outwardly toward the horn’s aperture. The electric field of the wave arriving at the aperture, which may vary as a function of xa and ya over the horn’s aperture, is called the electric-field aperture distribution or illumination,

## Slide 3
Inside the horn, wave propagation is guided by the horn’s geometry; but as the wave transitions from a guided wave into an unbounded wave, every point of its wavefront serves as a source of spherical secondary wavelets.
The aperture may then be represented as a distribution of isotropic radiators. At a distant point Q, the combination of all the waves arriving from all of these radiators constitutes the total wave that would be observed by a receiver placed at that point.
The radiation process described for the horn antenna is equally applicable to any aperture upon which an electromagnetic wave is incident.

## Slide 4: Examples of Aperture Sources
For example, if a light source is used to illuminate an opening in an opaque screen through a collimating lens, as shown in Fig. 9-21(a), the opening becomes a source of secondary spherical wavelets, much like the aperture of the horn antenna. In the case of the parabolic reflector shown in Fig. 9-21(b), it can be described in terms of an imaginary aperture representing the electric-field distribution across a plane in front of the reflector.

## Slide 5: Two types of mathematical formulations are available for computing the electromagnetic fields of waves radiated by apertures: a. Vector Formulation based on Maxwell’s equations- accurate, but mathematically involved. b. Scalar Formulation based on Kirchhoff’s work - easier to implement but restricted to large aperture dimensions (relative to the wavelength).
-Both methods are applicable at all wavelengths, including the visible spectrum.
-Validity of Scalar Formulation. The key requirement for the validity of the scalar formulation is that the antenna aperture be at least several wavelengths long along each of its principal dimensions.
We will limit our treatment to the scalar formulation.
A distinctive feature of such an antenna is its high directivity and correspondingly narrow beam, which makes it attractive for radar and free-space microwave communication systems.
The frequency range commonly used for such applications is the 1- to 30 GHz microwave band. Because the corresponding wavelength range is 30 to 1 cm, respectively, it is quite practical to construct and use antennas (in this frequency range) with aperture dimensions that are many wavelengths in size.

## Slide 6: Relating Radiated Field to Aperture Distribution

## Slide 9: Rectangular Aperture with Uniform Distribution

## Slide 14: Beamwidth

## Slide 18: Examples of Radiation Patterns
Circular aperture has circular beam
Cylindrical reflector has narrow beam along length direction and wide beam along its width direction
In each principal plane, beamwidth is inversely proportional to antenna dimension in that plane

## Slide 19: Directivity & Effective Area