## Slide 1: HEALTH RISKS OF EM FIELDS

## Slide 2
Can the use of cell phones cause cancer ?
Does exposure to the electromagnetic fields (EMFs) associated with power lines pose health risks to humans ?
Are we endangered by EMFs generated by home appliances, telephones, electrical wiring, and the myriad of electronic gadgets we use every day (Fig. TF17-1) ?

## Slide 3
Despite reports in some of the popular media alleging a causative relationship between low-level EMFs and many diseases, according to reports issued by governmental and professional boards in the U.S. and Europe, the answer is:
NO, we are not at risk, so long as manufacturers adhere to the approved governmental standards for maximum permissible exposure (MPE) levels.
With regard to cell phones, the official reports caution that their conclusions are limited to phone use of less than 15 years, since data for longer-term use is not yet available.

## Slide 4: Physiological Effects of EMFs
The energy carried by a photon with an EM frequency f is given by E = hf , where h is Planck’s constant.
The mode of interaction between a photon passing through a material and the material’s atoms or molecules is very much dependent on f . If f is greater than about Hz (which falls in the Ultraviolet (UV) band of the EM spectrum), the photon’s energy is sufficient to free an electron and remove it completely, thereby ionizing the affected atom or molecule.
Consequently, the energy carried by such EMwaves is called ionizing radiation, in contrast with non-ionizing radiation (Fig.TF17-2) whose photons may be able to cause an electron to move to a higher energy level, but not eject it from its host atom or molecule.

## Slide 6
Assessing health risks associated with exposure to EMFs is complicated by the number of variables involved, which include:
(1) the frequency f
(2) the intensities of the electric and magnetic fields
(3) the exposure duration, whether continuous or discontinuous, and whether
pulsed or uniform
(4) the specific part of the body that is getting exposed.
We know that intense laser illumination can cause corneal burn, high-level X-rays can damage living tissue and cause cancer and, in fact, any form of EM energy can be dangerous if the exposure level and/or duration exceed certain safety limits.

## Slide 7
Governmental and professional safety boards are tasked with establishing maximum permissible exposure (MPE) levels that protect human beings against adverse health effects associated with EMFs.
In the U.S., the relevant standards are IEEE Std C95.6 (dated 2002), which addresses EM fields in the 1 Hz to 3 kHz range, and IEEE Std 95.1 (dated 2005), which deals with the frequency range from 3 kHz to 300 GHz.
On the European side of the Atlantic, responsibility for establishing MPE levels resides with the Scientific Committee on Emerging and Newly Identified Health Risks (SCENIHR) of the European Commission.

## Slide 11
We are constantly bombarded by EM energy, from solar illumination to blackbody radiation emitted by all matter. Our bodies absorb, reflect, and emit EM energy all the time.
Living organisms, including humans, require exposure to EM radiation to survive, but excessive exposure can cause adverse effects. The term excessive exposure connotes a complicated set of relationships among such variables as field strength, exposure duration and mode (continuous, pulsed, etc.), body part, etc.
The emission standards established by the Federal Communications Commission in the U.S. and similar governmental bodies in other countries are based on a combination of epidemiological studies, experimental observations, and theoretical understanding of how EM energy interacts with biological material.
Generally speaking, the maximum permissible exposure levels specified by these standards are typically two orders of magnitude lower than the levels known to cause adverse effects, but in view of the multiplicity of variables involved, there is no guarantee that adhering to the standards will avoid health risks absolutely. The bottom line is: use common sense!

## Slide 12: Specific Absorption Rate (SAR)
The physical interaction of an RF EM wave with a biological material is complex, and it results in an inhomogeneous distribution of the induced EM field and the current density within the human tissue, despite the uniformity of the external exposure field.
The important fact that leads to a straightforward definition of the exposure parameter of relevance is the observation that only the EM energy absorbed by the human body can cause a bio effect.
Since the radiating part of the mobile phone and the human tissue (hand-head) are only a few millimeters apart in real usage, the evaluation of the exposure of a human in the near field of RF sources makes sense and it is accomplished by measuring the E-Field inside the body.

## Slide 13
SAR is used for the frequency range between 100 KHz and 10GHz and it depends on the geometry of the body part exposed to the EM waves and the location of the source of the energy. The design of a device as well as its operational frequency, antenna input power and orientation with respect to the body are important factors that affect SAR.
Example: If Electric field(rms)= 4 V/m, onductivity of material =150 S/m, mass density = 1250 Kg/ Then: SAR = 1.92 W/kg and Power Density = 0.042Kg/

## Slide 14: SAR Specifications and Standards
Different standards set different SAR threshold values to limit the potential health risk from EM radiation from mobile terminals. The maximum power deposition expressed in SAR, allowed by the FCC is 1.6 W/kg in 1g of tissue from exposure to cellular telephone radiation (US and Canada). On the other hand, the International Commission on Non-Ionizing Radiation Protection (ICNIRP) guidelines stipulate a maximum SAR of 2 W/kg in any 10 g of tissue in the head (EU, Japan and Brazil).

## Slide 15
SAR is a point quality and its value varies from one location to the other. Tissue density, conductivity and most significantly the E-Field are key parameters that determine the reliability and accuracy of a given SAR value. Normally, the average SAR is considered. We can see from Fig. 1 that the volume of interest is a cube around a point that expands in isotropic directions along the coordinate system until it contains 1g or 10g of tissue, and SAR values are then averaged in the cube.

## Slide 16
Comparing the FCC and ICNIRP standards for maximum of mass averaged SAR, it is worth mentioning that the volume of tissue used to define SAR can greatly influence the SAR values.
If the absorbed energy is averaged over a defined tissue of 10g, the result may be less strict comparing with the 1g averaged SAR. The latter performs more precise representation of the localized microwave energy absorption and a better
measure of SAR distribution inside the head.